## Slide 1: HLA architecture and performance improvements
MFC500/MFC431
www.continental-corporation.com
Chassis & Safety Division
Advanced Driver Assistance Systems

## Slide 2: HLA architecture – MFC400
Lights-Segmentation
Lights-Tracking and Classification
Lights-Interpretation
HLA parts
HLA function
RTE Out
Customer
Light list
Object list
Environment data
Headlight control
Memo
TLR
VCL
VCL
(CB)
FSD
(CB)
Norm
(SR)

## Slide 3: HLA architecture – MFC500
Lights-Segmentation
Lights-Tracking and Classification
HLA parts
HLA function
RTE Out
Customer
Light list
Object list
Headlight control
Scene perception
Scene interpretation (including HLA lights interpretation)
Scene description
Norm
HLA
LSD
Light Source
Detection

## Slide 4: HLA light segmentation I
 | MFC400 | MFC500
Tasks | Intensity segmentation: Find bright areas based on raw image raw2Lux conversion De-bayering for first color information Special handling for dark red and LED lights Search for paired lights Color segmentation: Find colored areas with certain brightness (red, yellow, green) based on raw, U, V and Sat image raw2Lux conversion Special handling LED lights | Light segmentation: Find bright areas with color information based on YUV+S images Adapt thresholds Special handling for LED lights Search for paired lights Traffic light handling (TLR post segmentation)
Active | Day: Only color segmentation (even image) Night: Both segmentations (odd image) | One segmentation for day (even image) and night (odd image)

## Slide 5: HLA light segmentation II
 | MFC400 | MFC500
Roi | Intensity segmentation: Width: ±19°, aprrox. 863 Height: approx. 327 Color segmentation: Width: Reduced ROI, i.e. 1024 Height: Top down to horizon, i.e. 256 | Whole reduced Roi Even image: 1024x482 Odd image: 1024x640
Inputs | Images (raw, U, V, S) IC | Images (Y, U, V, S)
Buffers | Each Segmentation: Lines: 800 Regions: 200 Lights: 150 | Estimation due to bigger ROI: Lines: 1200 Regions: 400 Lights: 300
Max Runtime (VME) | C674x: 2.56ms EVE: 5.67ms | Estimation: C674x: 5.00ms due to doubled buffers EVE: 9.00ms due to bigger ROI

## Slide 6: HLA light tracking
 | MFC400 | MFC500
Tasks | Predict track position across frames Associate intensity lights with tracks Find paired tracks Online calibration | Predict track position across frames Associate bright color lights with tracks Find paired tracks Online calibration
Active | Night | Day and night
Inputs | Light list Calibration data Vehicle data | Light list Calibration data Vehicle data
Buffers | Tracks: 35 Pairs: 12 | Tracks: 70 Pairs: 24
Max Runtime (VME) | C674x: 3.15ms | Estimation: C674x: 6.30ms due to doubled buffers

## Slide 7: HLA light classification I
 | MFC400 | MFC500
Tasks | Analyze tracks regarding intensity, color, position and motion Search for pulsed and truck lights Classify 3 tracks with LRF Decision regarding vehicles (ahead, oncoming), streetlamp and “neither-nor” | Analyze tracks regarding intensity, color, position and motion Search for pulsed and truck lights Classify all tracks with Vodca Preliminary decision regarding vehicles (ahead, oncoming), streetlamp, traffic light and “neither-nor” Headlight type determination
Active | Night | Day and night
Inputs | Track list Image (raw) Vehicle data | Track list Images (Y0, V1) Vehicle data
Buffers | LRF classifier: Ahead, oncoming, LED, streetlamps, red lights Color classifier | Classifier: Ahead, oncoming, LED, streetlamps, red lights, traffic lights (red, green, yellow, red-yellow), turn signals, break lights

## Slide 8: HLA light classification II
 | MFC400 | MFC500
Max Runtime (VME) | C674x: 1.22ms EVE: 0.80ms | C674x: LSD: 2.50ms due to doubled buffers Vodca: 70*30µs = 2.1ms EVE: Vodca: 70*25µs = 1.75ms

## Slide 9: HLA light interpretation
 | MFC400 | MFC500
Tasks | City detection Highway detection Traffic style detection Tunnel detection (also at day) Bright objects (dimming) Brightness determination | City detection (split between LSD and HLA) Highway detection (split between LSD and HLA) Traffic style detection Tunnel detection (also at day) Bright objects (dimming) Brightness determination
Active | Day and night | Day and night
Inputs | Track/Object list Image (raw) Vehicle data | Scene description (lights, road boundaries, map data, etc.) Images (Y0) Vehicle data
Max Runtime (VME) | C674x: 1.85ms City detection: 0.45ms Tunnel detection: 1.31ms | C674x: 1.5ms City: Written from scratch Tunnel: Optimized

## Slide 10: HLA function
 | MFC400 | MFC500
Tasks | Cluster objects to vehicles and define glare free areas Interpret environment and define high beam status and turn off reasons Dimming of headlights | Cluster objects to vehicles and define glare free areas Interpret environment and define high beam status and turn off reasons Dimming of headlights „LowBeam-LightingControl“ (Hell-Dunkel-Grenze Bestimmung für Lichtjustage)
Active | Night | Night
Inputs | Object list Environment data (city, highway, etc.) Vehicle data Blockage | Scene description (lights, road boundaries, vehicle objects, map data, etc.) Vehicle data Blockage
Max Runtime (VME) | C674x: 0.4ms | C674x: 0.8ms due to more data to analyze

## Slide 11: Steps / efforts to be done
Light segmentation:
  Merge intensity and color segmentation into one light segmentation
  Switch from raw to Y0 image
Light tracking:
  Integrate color light association
Light classification:
  Merge classification part of TLR into LSD
  LRF classifier: Switch toolchain to machine learning team (PED, VCL)
  Use Vodca for classification (GS update needed as well), i.e. switch also from LRF to HOG+LDP as used in Vodca 2.0
Light interpretation:
  Adaption to scene perception output. Some parts need to be re-designed
HLA function:
  Adaption to scene perception output. Needs to be completely re-designed

## Slide 12: Outlook and proposals
  Integrate radar objects and map data into scene perception
  All icons classified with all classifiers