## Slide 2: Generic SCons – Polyspace integration
- detailed description for usage
www.continental-corporation.com
Chassis & Safety Division
Advanced Driver Assistance Systems

## Slide 3: Generic Scons: Polyspace Integration - Overview
Introduction
  Generic SCons supports the generation of Polyspace projects for all C and CPP source. This manual describes the necessary configuration settings for enabling and usage of this feature.
Scope
  Applicable from Generic Scons Release AL_ETK_SCT_01.21.00 (CP 1.71) for generating Polyspace projects in 2012b (.cfg) or 2014b (.psprj) formats only.
  Applicable from Generic Scons Release AL_ETK_SCT_01.23.00 (CP 1.73) onwards for generating Polyspace project in 2016a (.psprj) format only.
  Current only DSP is support is enable in Release AL_ETK_SCT_01.23.00 (CP 1.73), future release will have DSP and ARM both.
  Generic Scons will not generate the compliance report either by Command line or using IDE.
Goal
  Generation of Polyspace project(s) for the code for
    DSP with C674x-compiler
    DSP with C66xx-compiler
    EVE with ARP32-compiler
    ARM Cortex A8 with TI-compiler/GCC
    ARM Cortex A15 with GCC
    Cortex M3 and M4

## Slide 4: Generic Scons: Polyspace Integration - Configuration
Shares
  The following shares need to be provided in the project:
    http://ims-adas:7001/si/viewproject?projectName=/nfs/projekte1/REPOSITORY/Base%5fDevelopment/05%5fAlgorithm/ETK%5fEngineeringToolKit/04%5fEngineering/SCT%5fSconstools/project.pj
    CP 1.71 for polyspace 2012b and 2014b or CP 1.73 onwards for polyspace 2016a
    as 02_Development_Tools\scons_tools.
Activation of Polyspace
  In order to activate the Polyspace project generation feature within Generic Scons, add the following line to 04_Engineering\03_Workspace\algo\<component>\sconstruct_config.scfg:
    generate_ps = True
    Note: By default generate_ps is False. This is needed at this moment to enable or disable the feature, so that users will not get unwanted warnings or errors during to polyspace project generation.

## Slide 5: Generic Scons: Polyspace Integration - Configuration
Source configuration
  Also, the following configuration items need to be updated in configuration files algo_config.scfg and algo_lib_file_list.scfg:
  # polyspace target options and language settings **** can be used for polyspace 2012b or 2014b or 2016a if required *****
  ps_target_option = {"-O": "0", "-OS-target": "Linux", "-batch": "true", "-dialect": "gnu3.4", "-post-analysis-command": "", "-to": "Software Safety Analysis level 0"}
  **** can be used only for polyspace 2012b or 2014b if required *****
  ps_lan_settings = {"-align": "32", "-default-sign-of-char": "signed", "-double-is-64bits": "", "-int-is-32bits": "", "-little-endian": "Little", "-long-long-is-64bits": "", "-pointer-is-32bits": ""}
  **** can be used for polyspace 2012b or 2014b or 2016a if needed to specify additional defines *****
  # polyspace macros
  ps_macros = ["NDEBUG", "__TI_COMPILER_VERSION__=5000000", "_LITTLE_ENDIAN", "__TI_EABI__=1", "_TMS320C6740", "__TMS320C6X__", "__STDC__", "__STDC_VERSION__=1", "__TI_32BIT_LONG__", "__SIZE_T_TYPE__=unsigned int", "__PTRDIFF_T_TYPE__=int", "_TMS320C6X", "restrict", "assert(X)="]
  # polyspace version
  ps_version = "2014"
    Note: "2012" or "2014“ (CP 1.71) or "2016a“, by default "2016a“ in CP 1.73 onwards
  # polyspace additional includes **** can be used for polyspace 2012b or 2014b or 2016a if required *****
  ps_additional_includes = Split(xxx_algo_ps_additional_include_paths)
  # polyspace additional sources **** can be used for polyspace 2012b or 2014b or 2016a if required *****
  ps_additional_sources = Split(xxx_algo_ps_additional_sources)
  Notes:
  1) Where "xxx" is a component name
  2) Refer scons_templates\01_Source_Code\algo\xxx\algo_config.scfg and algo_lib_file_list.scfg.

## Slide 6: Generic Scons: Polyspace Integration – via Commandline
Polyspace Aliases for 2012 or 2014
  Aliases in Generic SCons: The following aliases would be supported:
    xxx_ps : Proceduces all Polyspace projects ONLY for all <arch>
      xxx_ps_<arch>_proj: Generate Polyspace project ONLY for the <arch>
Polyspace Aliases for 2016a
  Aliases in Generic SCons: The following aliases would be supported:
    xxx_ps : Proceduces all Polyspace projects
      xxx_ps_2016a_proj: Generate Polyspace project ONLY for the 2016a
    where xxx stands for the component resp. algo and <arch> = “ti_c674x“, “ti_c66xx“, “ti_arp32“, “ti_cortex_a8“, “ti_cortex_a15“, “ti_cortex_m3“ and “ti_cortex_m4“
    Note: No analysis takes place and no reports are generated.

## Slide 7: Generic Scons: Polyspace 2012 or 2014 Integration – via Commandline
  Should use the GSCons checkpoint 1.71.
  via Command line
    "scons.bat xxx_ps_<arch>“ from 03_Workspace\algo\xxx:
      Generates the Polyspace project file in 05_Testing\05_Test_Environment\algo\modtests\ps_tests\xxx
      Source code analysis for <arch> with corresponding configuration settings; analysis results will be stored in 05_Testing\05_Test_Environment\algo\modtests\ps_tests\xxx\xxx_<C/CPP>_<arch>_precise
    During generation of polyspace projects all configuration warnings and errors are displayed on command line if any
  via Polyspace IDE
    At this moment, the generated Polyspace projects will be run in Polyspace IDE due to license issue.

## Slide 8: Generic Scons: Polyspace 2016a Integration – via Commandline
  Should use the GSCons checkpoint 1.73 onwards.
  via Command line
    "scons.bat xxx_ps or xxx_ps_2016a_proj “ from 03_Workspace\algo\xxx:
      Generates the Polyspace project file in 05_Testing\05_Test_Environment\algo\modtests\polyspace\xxx
      Source code analysis for all <arch> with corresponding configuration settings; analysis results will be stored in 05_Testing\05_Test_Environment\algo\modtests\polyspace\xxx\AllFiles\Result
  via Polyspace IDE
    At this moment, the generated Polyspace projects will be updated manually by polyspace experts and run in Polyspace IDE due to license issue.

## Slide 9: Thank you
for your attention!